| Formula RS |  |
| --- | --- |
|  | 12.06.2002 |

DESCRIPTION

Castrol Formula RS 10W-60 is a fully synthetic engine oil that offers exceptional engine protection in performance driving conditions.

APPLICATION

Castrol Formula RS 10W-60 is race proven for high temperature protection and high performance.

FEATURES/BENEFITS

Castrol Formula RS 10W-60 contains significantly lower levels of organochlorine allowing safer and easier recycling and disposal. It aids your engine in operating cleanly with reduced emissions and reduced noise levels. Low viscous drag ensures superb cold start and rapid circulation in sub-zero temperatures.

PERFORMANCE

API		SL / CF

ACEA		A3/B3

TYPICAL CHARACTERISTICS

Appearance	bright, clear, dark

SAE Viscosity Rating	10W-60

Relative Density @ 15.6º C	0.852

Viscosity @  40º C,  mm²/s	154.4

Viscosity @ 100º C, mm²/s	22.57

Viscosity Index	175

Flash Point  (closed) º C	206

Pour Point º C	below -36

TBN	10.14